## Slide 1: Flow Cytometry
Next Generation Pathology Lectures
Paul D. Simonson, M.D., Ph.D.
Weill Cornell Medicine
September 23, 2021, Room C405, 5 p.m. to 6:30 p.m.

## Slide 2: Pre-requisites for following the exercises
Install FlowJo (available for Mac and Windows)
  Download and install FlowJo from https://www.flowjo.com/solutions/flowjo/downloads
  Activate 30-day free trial at https://www.flowjo.com/solutions/flowjo/free-trial (it may take up to one day for the trial serial number to be activated!)
    OR choose student license (free)
    OR paid licenses are also available through WCM ($250 per year)
Install R, Rstudio, and R packages (available for Mac, Windows, and Linux)
  Install R if it is not installed already. One option is to follow the instructions found here: http://lib.stat.cmu.edu/R/CRAN/
  Download and install RStudio Desktop (open source license, free) from https://www.rstudio.com/products/rstudio/download/.
  Install the packages necessary to make an R Notebook.
    Within Rstudio, choose File > New File > R Notebook
    If the necessary packages are not installed, Rstudio will ask for permission to install them. Allow them to be installed.
  Within Rstudio, install the “flowCore” package. Follow the installation instructions found here (enter commands in the “Console” tab): https://www.bioconductor.org/packages/release/bioc/html/flowCore.html.
  Install the “umap” package by entering the following in the “Console” tab: install.packages(“umap”)

## Slide 3: Objectives
Basic introduction to flow cytometry (technique, applications, etc.)
Discuss and apply basic gating to flow cytometry data
Discuss and apply the UMAP algorithm to flow cytometry data
Discuss supervised machine learning for flow cytometry

## Slide 4: Clinical Flow Cytometry
Commonly performed flow cytometry tests:
  Lymphocyte subset enumeration
    CD4 subsets (HIV), immunodeficiency
  CD3 expression (solid organ transplant)
  CD34 stem cell (blast) enumeration
  Reticulocyte enumeration
  Paroxysmal nocturnal hemoglobinuria (PNH) testing
  DNA cell cycle / ploidy analysis
  Leukemia/lymphoma immunophenotyping
Notes: Rapid robust multiparameter analysis of single cells
By measure fluoresence intensity produced by fluorochrome labeled antibodies binding to targeted cell specific proteins
On this platform numerous assays can be performed allowing for such clinical uses as

## Slide 5: A quick introduction to flow cytometry
Uses panels of fluorescent antibodies and light scattering to characterize single cells as they pass through a capillary tube
Helpful in diagnosing leukemia, lymphoma, etc.
Interpretation of data is performed by hematopathologists by “gating” and visual interpretation of data

## Slide 6: Advantages of flow cytometry
Can analyze millions of cells from a single sample
  Good for finding rare cell types
  Makes good use of small biopsy specimens
Rapid
Quantitative
Flexible
Notes: The power of single cell analysis is compounded by the
ability to measure multiple parameters simultaneously on each individual cell, to do this very fast (in excess
of 20,000 cells/second), and to isolate/purify/sort desired subpopulations

## Slide 8: What is light scatter?
Photons pass through a cell and get “scattered” in different directions.
What we measure in flow cytometry:
  0o light scatter (forward scatter)
    Related to cell size (higher forward scatter = larger cells)
    Decreases as cells degenerate
  90o light scatter (side scatter)
    Related to cell cytoplasmic granularity/complexity
    Decreases as cells degenerate

## Slide 9: What is fluorescence?
Light of a short wavelength is absorbed by a molecule and re-emitted at a longer wavelength.
The fluorescent molecules used in laboratory work are often referred to as “fluorophores” or “fluorochromes.”
Fluorophores can be attached to antibodies, which are used to detect antigens in cells.

## Slide 10: Common fluorochromes
From Becton-Dickinson Web Site
Notes: A general guideline for the relative intensities of the various fluorochromes is, from brightest to dimmest, PE, PE-Cy 7, PE-Cy5, APC, APC-Cy7, Alexa Fluor 647®, Alexa Fluor 700®, FITC, Pacific Blue, Alexa Fluor 488®. This is a general pattern; some differences in the relative intensities are seen for individual antibodies.

## Slide 11: How to detect fluorescence from multiple fluorophores: series of selectively reflective mirrors and light filters
Notes: Forward and side scattered light and fluorescence from stained cells are split into defined wavelengths and channeled by a set of filters and mirrors within the flow cytometer. The fluorescent light is filtered so that each sensor will detect fluorescence only at a specified wavelength. These sensors are called photomultiplying tubes (PMTs).

## Slide 12: Acquired signals
As cell passes through the detector, the signal intensity gradually increases, then decreases
Values stored by the computer:
  Signal height: maximum signal intensity (i.e., the “peak” value)
  Signal area: total “area under the curve”
    Useful for detecting two cells that are passing through at nearly the same time
Notes: AAs the fluorescent labeled cell passes through the optics and is interrogated by the laser, photons are emitted and so the intensity of the voltage measured increases. As each fluorescing cell completes its path through the laser beam, this leaves a pulse of voltage over time based on number of photons emitted over time. These are detected by the PMT and converted to a voltage pulse, known as an event. The total pulse height and area is measured by the flow cytometer. The measured voltage pulse area will correlate directly to the intensity of fluorescence for that event.

## Slide 13: The summarized output: “dot plots”/histograms
Each point corresponds to a single cell or cluster of similar cells
2-dimensional scatter plots are made for different pairs of antigens

## Slide 14: Considerations for designing flow cytometry antibody panels

## Slide 15: CD (Cluster Designation) antigens correspond to antigens on cell surfaces
Examples: CD3, CD20, CD45, etc.
Cell surface antigens are used because they are easy to detect (no permeabilization of cell membrane required)
Biooncology.com

## Slide 16: Commonly Used CD Antigens
CD Antigen | Cell type
CD3 | T cells
CD4 | Helper T cells, monocytes
CD8 | Cytotoxic T cells
CD16, CD56 | NK cells
CD19, CD20 | B cells
CD13, CD33 | Myelomonocytic cells
CD34 | Stem cells
CD64 | Monocytes
CD14 | Mature mononocytes

## Slide 17: Example Panels of Antibodies
 | PB | FITC | PE | PE-TR | PE55 | PE7 | A594 | APC | A700 | APC7
B cells | CD45 | k | l | CD19 | CD34 | CD20 | CD38 | CD10 | - | CD5
T cells | CD45 | CD2 | CD7 | CD34 | CD8 | CD3 | CD4 | CD56 | - | CD5
Blasts | HLA-DR | CD15 | CD33 | CD19 | CD117 | CD13 | CD38 | CD34 | CD71 | CD45
Myeloid | HLA-DR | CD64 | CD123 | CD4 | CD14 | CD13 | CD38 | CD34 | CD16 | CD45
Panel names
Fluorochromes and antibodies

## Slide 18
FITC = Green
PE = Orange
Excitation = Dotted
Emission = Solid
The need for fluorophore compensation
Fluorochromes do not emit light at just one wavelength. They have emission spectra.
Emission spectra for similar fluorophores can overlap.
The overlap will result in light being detected in more than one channel, even though only one fluorochrome is present.
Mathematical “compensation” is applied to correct for the overlap detected in multiple detector channels.

## Slide 19: Lack of Compensation
After compensation

## Slide 20: Collection/storage of cells
Of anticoagulants, cells are best stored in heparin
RPMI is a cell nutrient solution that helps maintain cell viability
Refrigeration slows degradation
Some cells degrade faster than other cells
Commons.Wikimedia.org

## Slide 21: Sample processing
100 ml whole blood
Add antibodies
Incubate
Add red blood cell lysing reagent and incubate
Wash to remove debris and lysing reagent
Fix in paraformaldehyde (optional)
Send it through the flow cytometer!
Commons.Wikimedia.org
Notes: n direct immunofluorescence staining, cells are incubated with an antibody directly conjugated to a fluorochrome (e.g. FITC). This has the advantage of requiring only one antibody incubation step and eliminates the possibility of non-specific binding from a secondary antibody.

## Slide 22: Quiz
In flow cytometry, increased forward scatter usually indicates:
a. Increased cell size
b. Decreased cell maturity
c. Increased cell complexity
d. Decreased cytoplasmic granularity

## Slide 23: Variants of flow cytometry
Hematology analyzers (for measuring CBC): No fluorescence, but measures scattering and electrical impedance
CyTOF: Flow cytometry combined with mass spectrometry for detection (instead of fluorescence). Subject of a later lecture…
Bead assays: Fluorescent beads with antibodies attached are measured, not cells.

## Slide 24: Bead assays
Beads are designed to have unique combination of fluorophores and intensities
Using a sandwich approach, analytes can be detected (cytokines, etc.)
https://www.bdbiosciences.com/content/dam/bdb/marketing-documents/CBA_Brochure_Intl.pdf

## Slide 25: Analyzing the Data

## Slide 26: Pattern recognition
55 unique combinations

## Slide 27: Normal B cell Maturation
Wood and Borowitz (2006) Henry’s Laboratory Medicine

## Slide 28: Normal T cell Maturation
Wood and Borowitz (2006) Henry’s Laboratory Medicine

## Slide 29: Normal Myeloid Cell Maturation
Wood and Borowitz (2006) Henry’s Laboratory Medicine

## Slide 30: Gating
Identifies a subgroups of data points within the dataset
Usually performed graphically on histograms
Boolean logic used to combine gates
  And, Or, Not, etc.

## Slide 31: Inferential reasoning
Inference is less preferred since sometimes our assumptions are incorrect, and we cannot apply it to individual cells.
Solution: Build flow cytometers with more detector channels
18%
80%
66%
0.4%
Sometimes we want to run more antibodies than the machine can handle. We then have to run two tubes of antibodies with cells and infer whether one cell population in one tube is the same as that in another tube for the two antibody panel tests.

## Slide 32: Letting a computer identify the cell populations for us
Unsupervised machine learning (no data annotation): finds patterns, associations, clusters, etc.
  GMM, FlowSOM, SPADE, etc.
  t-SNE
  UMAP

## Slide 33: The increasing need for clustering algorithms
More colors --> more scatter plots --> more complex analysis for humans
"Contamination" of gates
Unsupervised clustering:
  Considers all parameters at once to find cells that are similar to each other
  Creates low-dimensional representations that are easier to interpret by humans
  Makes it easier to cleanly parse populations
Notes: Flow case: patient with a history of lambda+ mantle cell lymphoma who has undergone treatment that includes rituximab.

## Slide 34: What is t-SNE?
https://www.oreilly.com/content/an-illustrated-introduction-to-the-t-sne-algorithm/
Converts high-dimensional data to clusters in two-dimensions
Dissimilar clusters are (generally) farther apart
Already available in some commercial flow cytometry software
Drawback: For each data set, the clusters end up in different locations
Notes: When we consider that the number of 2D scatter plots increases exponentially with the number of parameters, which are increasing as new 20-color flow instruments are becoming more common, the utility of finding new ways to represent this higher dimensional data in two-dimensional plots becomes clear.

## Slide 35: Interpreting t-SNE clusters by marker intensity
https://marissafahlberg.com/a-basic-overview-of-using-t-sne-to-analyze-flow-cytometry-data/​

## Slide 36: Interpreting t-SNE clusters by gating
Example: Bone marrow involved by CLL (86% of cellularity)
T-SNE calculated using:
  FSC-H,
  SSC-H
  sKappa
  SLambda
  CD5
  CD23
  CD10
  CD20
  CD19
  CD45
Notes: 5 min 12 s

## Slide 37: Using t-SNE to optimize an AML MRD panel
Dissimilar cell populations are farther apart
Better choices of antibodies can make the separations cleaner
Changing antibody panels and looking at MRD population separation by t-SNE made a better panel
Coustan-Smith E et al. Universal monitoring of minimal residual disease in acute myeloid leukemia. JCI Insight. 2018;3(9):e98561.
Notes: https://insight.jci.org/articles/view/98561/figure/7

## Slide 38: UMAP
Reduces high-dimensional data to two-dimensional representations
Better preserves relationships between cells and clusters
"Embeddings" can be saved and used again with data from new samples --> cell populations will show up in the expected locations
Bone marrow involved by CLL (86% of cellularity)
Notes: 52.7 s to compute, 100,000 cells

## Slide 39: Example gating using UMAP
*Same as for prior t-SNE.
UMAP calculated using*:
  FSC-H
  SSC-H
  sKappa
  sLambda
  CD5
  CD23
  CD10
  CD20
  CD19
  CD45

## Slide 40: Comparing t-SNE and UMAP...

## Slide 41: Exercises

## Slide 42: FlowJo Exercise: Basic Gating
Open FlowJo.
Drag the folder “CLL” into the FlowJo window.
Go to “Preferences > Workspace > Sample Display Naming” and choose “Use Short File Name”
We will make the following gates using the “B1” antibody panel data:
  White Cells
  Lymphocytes
  B cells
  Kappa light chain expression
  Lambda light chain expression
Helpful video for basic introduction to FlowJo: https://www.youtube.com/watch?v=Ux0S0g6-Fvs

## Slide 43: Download and unzip the GitHub repository
https://github.com/SimonsonLab/2021_Next_Gen_Flow_Lecture

## Slide 44: Now we try it…
We will use files from publicly available data (https://flowrepository.org/id/FR-FCM-Z2JW).
“Singlets” and compensation were already performed for these data. Viability dye was not used.
Open FlowJo and drag the “CLL” folder (from “ExampleData” folder) into the open window.
Double-click on the second file in the list.
Draw a gate around the CD45-positive cells (white cells).
Double-click inside the gate to get ready for the next step.

## Slide 45: Now gate lymphocytes, monocytes, and granulocytes…
Set the x axis to side scatter (look for SS-A) and the y axis to CD45.
Lymphocytes have the least side scatter.
Try exploring the axes options by clicking on the large “T” buttons.

## Slide 46: Gate B cells using CD19
Set the x axis to side scatter (look for SS-A) and the y axis to CD19.
B cells have high CD19 expression.

## Slide 47: Find the kappa and lambda restricted B cell distributions

## Slide 48: Create a report using the Layout Editor

## Slide 49: Create a UMAP of flow cytometry data
Open the file “rstudio notebook.Rmd” in RStudio and run it.

## Slide 50: Open the generated FCS file in FlowJo
Try drawing gates around the populations seen in the UMAP plot (set UMAP x on the x axis and UMAP y on the y axis) and see how those populations compare with the lymphocytes, monocytes, and granulocytes gated using the traditional gating approach.